## Slide 1: SecuriSens LIST & d-LIST
Sales Presentation
Release: (06)

## Slide 2: LISTEC Linear Heat Detectors Content
Principle of Operation
Application Drivers
Portfolio
Strength
Specifications
Success Stories

## Slide 3: PRINCIPLE OF OPERATION Embedded Heat Sensors
SPACING
SEC 15: 1, 2, 3, 4, 5 or 10 m
SEC 20: 2, 3, 4, 5, 8 or 10 m
... or to your specification
ALUMINIUM SHIELD
  MEASUREMENT
  10s intervals
  0.1 resolution
  Repeatability ±0.1K
  Installation Properties
  Radius as small as
    25cm (SEC 15)
    30cm (SEC 20)
  Cable Properties
  Aluminium Foil Shield
  Reinforced (strain relief)

## Slide 4: PORTFOLIO System Components
4 (+16)
RELAYS
RS 485
CBO 15
SCU 835
SEC 15
2x350 m, 2x100 Sensors
SEC 15 (d-LIST)
SEC 20
RS 232 (MODBUS RTU) / ETHERNET (Modbus TCP)
3.2km, 320 Sensors
7 (+256)
RELAYS
SEC 20
CBO 20
1200m
247 units
  LISTCONTROLLER
RS 485 (MODBUS RTU)
ETHERNET (MODBUS TCP)
SCADA System
Building Management System
UPDATE
CBO 15
CC 15

## Slide 5: PORTFOLIO System Overview
CBO 15
Sensor Control Unit
SCU 835
Max. 750 m, 200 Sensors
SEC 15 (d-LIST)
SEC 20
Max. 3.2 km, 320 Sensors
CBO 20
  LISTCONTROLLER
TEMPERATURE MONITORING
EN54-22 A1N, A2N, BN, CN, ATEX Zone 2/22
700 m (2 x 350 m)
1 / 2 / 3 / 4 / 5 / 10 m or to specification
15 mm
Typical Application
Compliance
Max. Length
Sensor Spacing
Cable Diameter
FIRE DETECTION
EN54-22 A1N, A2N, BN, ATEX Zone 2/22
3’200 m
2 / 3 / 4 / 5 / 8 / 10 m or to specification
18 mm

## Slide 6: APPLICATION DRIVER Long Distances
  Long Distance Monitoring
    Road / Rail Tunnels
    Utility Tunnels
    Cable Trays
    Pipelines
    Conveyor Belts

## Slide 7: APPLICATION DRIVER Harsh Environment
  Works under extreme conditions
    Rain / Moisture
    Dirt / Dust
    Heat / Frost
    Wind
    Aggressive Gases
    EMI
    Insects

## Slide 8: APPLICATION DRIVER Large Area
  Up to 320 parking lots per cable
    Extensive Coverage
    Pollution resistant
    Humidity resistance
    Maintenance friendly
    Zero nuisance alarms

## Slide 9: STRENGTH Flame retardant
  Flame retardant and halogen free
    Hospitals
    Rail Stations
    Car Parks
    Assembly Halls
5 Min.
10 Min.
15 Min.
20 Min.
25 Min.
30 Min.
0
LIFE SAVING QUALITY

## Slide 10: STRENGTH Monitoring

## Slide 11: STRENGTH Point Accuracy
  Reliable, accurate and stable
    IR sensitive sensors
    Clear sensor position
    No drift no re-calibration
    Measurement Res. 0.1C
THERMOGRAPHIC IMAGE

## Slide 12: STRENGTH Accurate Zoning
Sensor 1 2 3 4 5 6 7 8 9 10 11 12 13
VALVE 1
VALVE 2
VALVE 3
Zone 1
Zone 2
Zone 3

## Slide 13: STRENGTH Zone Stability
Fiberoptic: Drift Buffer required
for reliable zoning
VALVE 1
VALVE 2
VALVE 3
Regular calibration needed
to maintain zone accuracy
Zone 1
Zone 2
Zone 3
Min. Length of the coil:
6 x Spatial Resolution
Notes: “For an unambiguous mapping of events we recommend using an extra length of sensor cable of at least six times the spatial resolution in between the alarm zones.” (Siemens Planning Guide)

## Slide 14
Question
Is the following statement true?
Absolute precise location and measurement accuracy are strengths of the LISTEC Linear Heat Detectors.

## Slide 15: STRENGTH Installer friendly
  Normal cable properties
   no specialists needed
   field repairable
   no limits to cuts & repairs
    Standard electrical tools

## Slide 16: STRENGTH Maintenance free
  Less Traffic Shut Downs
   Best Total Cost
  of Ownership
    No drift
     no re-calibration
    Performs self-test
     no maintenance test
    Firmware based
     no annual fee for software licensing

## Slide 17: STRENGTH Nearly Unlimited Repair
  LIST Cables
    Full performance no matter how many repair patches
    Easy to repair by simple connection boxes or even cable sleeve joints
    No cable extension required for repair
  Fiber Optics
  Limited number of splices according to “Loss Budget Calculation” (next slide)
  Precise work by specialist company only
  2 Splice boxes and 2 cable coils per repair
  Subsequent re-calibration required (resolution and zoning)
  Time consuming and expensive (tunnel shut downs)
Notes: FibroLaser Maintenance & Repair Manual:
“Cut out the damaged sensor cable section and replace it with a new cable. Use two splice boxes for this.
“The slice work may only be performed by a qualified specialist company.”
“Following the repair, the zones must be checked and must be adjusted.”

## Slide 18: STRENGTH No “Loss Budget”
  Fiber Cable’s Loss Budget
FIBER CORE
CLADDING
(reflector)
Sensitivity
of the receiver
1km
2km
3km
4km
5km
6km
7km
8km
9km
Signal Level
Low
High
Connector Loss
Normal Cable Loss
typically 0.4dB/km
Absorption Loss
Scattering Loss
Heterogeneous
Structures Loss
Bending Loss
Splicing Loss
typically 0.3dB
Splicing has a huge impact on cable length
1 Repair = 2 splices = 300m loss
(reduced total length of cable)
typically 0.3dB
Notes: FibroLaser Maintenance & Repair Manual:
“Cut out the damaged sensor cable section and replace it with a new cable. Use two splice boxes for this.
“The slice work may only be performed by a qualified specialist company.”
“Following the repair, the zones must be checked and must be adjusted.”

## Slide 19
Question
Which of the following answers is true?
The Loss Budget of LISTEC Linear Heat Detectors is
- zero
- infinite
- irrelevant

## Slide 20: STRENGTH Water resistant
  Easy to clean
   Mechanically and
  chemically resistant
    Water / Moisture
    Gases / Pollution
    Tensions / Shocks

## Slide 21: STRENGTH High EMI Immunity
    Tested and approved for heavy duty applications
    (railway or power transmission)
  Heavy Duty
0.5m

## Slide 22: STRENGTH Max. & Diff. Alarms
  Pre-Alarms for Early Warning
24h Temperature Profile
  Difference Alarm
  Difference to Normal
  Difference Pre-Signal
  in % of the Diff-Alarm
  Max. Alarm
  Difference to 0°C
  Max. Pre-Signal
  in % of the Threshold-Alarm
  Settings are per Zone
  Addressable
Max. Alarm
Diff. Alarm

## Slide 23: STRENGTH Multiple Alarms
  Progressive Response
Difference
Pre-Signal
Alarm
(Diff. or Threshold)
Verify the alert
Locate the cause
Call Emergency Team
Stop the trafic
Evacuate the site
Initiate fire alarm
1
2

## Slide 24: STRENGTH Branching
  Total Flexibility
  To place branches
  To add branches later on

## Slide 25: STRENGTH Failsafe
  Loop Topology:
  Detector addressing from both sides
  Full detection capability even in case of a cable cut
One cut – zero impact

## Slide 26: STRENGTH Controller Position
  Total Flexibility
  to connect the controller

## Slide 27: STRENGTH [SEC 15] Single Sensors
  Equipment Monitoring
  Engines
  Heating units
  Ovens
  Cooling devices
  Environment Monitoring
  Open air
  Loading docks
  Semi-covered facilities
  (Car Parks, Storage)
  In-duct Monitoring
  Ventilation systems
  Air handling units

## Slide 28: STRENGTH [SEC 20] Status Monitoring
  8 Inputs
  Opto-coupler isolated
  5 … 28VDC
  Application Examples
  Read Door Contacts
  Read Smoke Switches
  Read 3rd Party Alarm Outputs
  Check Valve Position
8 Inputs

## Slide 29: STRENGTH Networking
  SCU 835
  RS485 / Modbus RTU / 247 Participants
  LISTCONTROLLER
  32 Participants
  Ethernet (Modbus TCP)
  RS232 (Modbus RTU)
  Management System / Visualization
  RS485 (Modbus RTU)

## Slide 30: ACCESSORIES Cable Fixings

## Slide 31: SPECIFICATIONS Control Units
Criteria | SCU 835 | LISTCONTROLLER
Sensors per unit | 200 (2x100) | 350 (320 with VdS)
Sensor ID (physical address) | 1 – 65’536 | 1 - 999
Zones per system (logical assignment) | 1 - 64 | 1 - 254
Redundancy / Loop | no | yes / yes
Relays (monitored 48VDC/250mA) | 4 (+16) | 7 (+256)
Measurement Temp. Range | -40°C to +120°C | -40°C to +200°C
Operating Temp. Range | -25°c to +70°C | -25°C to +70°C
Protection Class | IP 65 | IP 54
Power Requirements | 10.5 … 30 VDC / 5.5 W | 9.5 … 36 VDC / 5 W
Networking (LISTnet, up to nn units) | RS485 or Ethernet, up 247 units | RS485 or Ethernet, up to 32 units
Management System I/F | RS232 / RS485 / Ethernet | RS232 / Ethernet
Programming & Data Communication | RS232 / RS485 / Ethernet / USB | RS232 / Ethernet / USB
Data Logging Port | RS232 / RS 485 / Ethernet | RS232 / Ethernet
Max. Number of Events in Memory | 1000 | 450
Approvals | VdS | VdS, ATEX

## Slide 32: SPECIFICATIONS Sensor Cables
Criteria | SEC 15 (d-LIST) | SEC 20
Max. Cable Length | 700 m (2x350 m) | 3’200 m
Typical use | Industry, belt conveyors, elevators | Road & Rail Tunnels, long belt conveyors
Sensor Spacing | 1 / 2 / 3 / 4 / 5 / 10 m | 2 / 4 / 5 / 6 / 8 / 10 m
Measurement Temp. Range | -40°C to +120°C | -40°C to +200°C
Resolution (Measurement Reading) | 0.1°C | 0.1°C
Operating Temp. Range | Continuous: -40°C to +85°C / Short term: up to max. meas. temperature | 
Cable Diameter | 15 mm | 18 mm
Min. Bending Radius | 25 cm | 30 cm
Max. Number of Sensors | 200 (2x100) | 350 (320 VdS), 500 temp. monitoring
Sensor Type | Embedded temperature sensor, semiconductor | 
Certification | EN54-22 Cl. A1N, A2N, BN, CN, ATEX Zone 2/22 | EN54-22 Cl. A1N, A2N, BN, ATEX Zone 2/22
Reinforced, Aluminium shielded, flame retardant and halogen free cables.

## Slide 33: SUCCESS STORIES Fréjus, France - Italy
  Road Tunnel
  13km
  Sensor Cable Length: 12’800m

## Slide 34: SUCCESS STORIES Bypass, Neuchâtel, Switzerland
  Road Tunnel
  7’100m
  Sensor Cable Length: 14’200m

## Slide 35: SUCCESS STORIES A86, Paris, France
  Double Deck
  Road Tunnel
  10km in 2 sections
  Sensor Cable Length: 10’400m

## Slide 36: SUCCESS STORIES El Sinaloense, Durango, Mexico
  Road Tunnel
  2’787m
  Sensor Cable Length: 2’794m

## Slide 37: SUCCESS STORIES Senador Nelson Carneiro, Rio de Janeiro, Brazil
  Road Tunnel
  1’800m
  Sensor Cable Length: 3’800m

## Slide 38: SUCCESS STORIES Södra Länken, Stockholm, Sweden
  Road Tunnel
  4’700m
  Sensor Cable Length: 10’400m

## Slide 39: SUCCESS STORIES Göta, Gothenburg, Sweden
  Road Tunnel
  1’600m
  Sensor Cable Length: 3’400m

## Slide 40: SUCCESS STORIES Port tunnel, Dublin, Ireland
  Road Tunnel
  4’500m
  Sensor Cable Length: 8’900m

## Slide 41: SUCCESS STORIES M30 Airport, Madrid, Spain
  Road Tunnel
  1’306m
  Sensor Cable Length: 2’600m

## Slide 42: SUCCESS STORIES Al-Azhar, Cairo, Egypt
  Road Tunnel
  2’700m
  Sensor Cable Length: 2’330m

## Slide 43: SUCCESS STORIES Elbtunnel, Hamburg, Germany
  Road Tunnel
  12’400m
  Sensor Cable Length: 11’600m

## Slide 44: SUCCESS STORIES Engelberg, Stuttgart, Germany
  Road Tunnel
  2’530m
  Sensor Cable Length: 5’000m

## Slide 45: SUCCESS STORIES Coschützer, Dresden, Germany
  Road Tunnel
  2’332m
  Sensor Cable Length: 4’600m

## Slide 46: SUCCESS STORIES Königshainer Berge, Görlitz, Germany
  Road Tunnel
  3’281m
  Sensor Cable Length: 6’562m

## Slide 47: SUCCESS STORIES Berg Bock, Suhl, Germany
  Road Tunnel
  2’738m
  Sensor Cable Length: 5’500m

## Slide 48: SUCCESS STORIES Josef Deimer, Landshut, Germany
  Road Tunnel
  1’470m
  Sensor Cable Length: 1’470m

## Slide 49: SUCCESS STORIES Wambel, Dortmund, Germany
  Road Tunnel
  1’420m
  Sensor Cable Length: 3’260m

## Slide 50: SUCCESS STORIES Bypass Tunnel, Sochi, Russia
  Road Tunnel
  2’600m
  Sensor Cable Length: 5’350m

## Slide 51: SUCCESS STORIES Metro Station, Düsseldorf, Germany
  Fire Detection at the Station “Heinrich-Heine-Allee”

## Slide 52: SUCCESS STORIES Garbage Incinerator, Bremerhaven, Germany
  Heat Monitoring of Conveying Systems

## Slide 53: SUCCESS STORIES Saarbergwerke, Völklingen, Germany
  Heat Monitoring of Conveying Systems

## Slide 54: SUCCESS STORIES Coal Power Station, Patnow, Poland
  Heat Monitoring of Conveying Systems

## Slide 55
Thank You!
Securiton AG
Alpenstrasse 20
CH – 3052 Zollikofen
www.securiton.com
+41 58 910 50 50
Industrial grade
HEAT MONITORING
and
FIRE DETECTION